# zCore user manual

version	2.1
date	2014.10.23
maintain	lokisz@yahoo.com
Release range	public
Scope	Hardware and software developers

date	version	Change Log
2011.5.4	1.0	initial version
2011.5.10	1.1	STA updates and registers uartlite exemplary precautions; analog portion of increase instructions described; PSS increases the storage space allocation instructions;
2011.5.16	1.2	Update ocm restrictions description of the program; zCore increase support dcr, dcr determine uic and uartlite of address assignment. Modify uartlite example.
2011.5.17	1.3	Hardware update ocm design, unified instruction and data ocm, supports read and write, and execute.
2011.9.29	2.0	EDK and other modifications described based on product plans, removal of part of UIC explained, the increase Implementation Guide section.
2014.10.23	2.1	Update and maintain e-mail mailing list and increase revenue

## 1 Introduction
zCore originally PWRSemi processor IP core family of processors for the embedded market development, currently GPLv2 open-source license (https://groups.yahoo.com/neo/groups/openzcore/info), ZCore transparent compatible processor PowerPC / Power Architecture instruction set. The main contents of this manual explains how to zCore system software and application development.
The second section will be mainly described zCore architecture and programming considerations, different software developers are required to achieve the basis zCore, initialize parameters and corresponding configuration compiler to avoid unimplemented instruction and performance optimizer.
The third section will be mainly described zCore processor subsystem (PSS) of the hardware architecture, the PSS to complete a simple system, comprising a processor core, an on-chip memory, timers, interrupt controller portion and UART communication module.
The fourth section describes the integration of PSS, other on-chip peripheral bus, and a reference IP SoC system.
The fifth specific use EDK entry-level internet -XUPv2P hardware platform will be described, and the respective functions include onboard resources defined, such as LED lights, and switches. Wherein the onboard FPGA chip for implementing the reference SoC system.
## 2, zCore architecture and programming
zCore architecture adheres "The IBM PowerPC Embedded Environment: Architectural Specifications for IBM PowerPC Embedded Controllers" specification [1], with reference to the specific implementation of processor cores user manual IBM ppc405 [2].
According to all the instructions to achieve the features and compatibility needed Power Architecture, zCore will ppc405 support the set is divided into I, II, III three categories. Wherein the instruction is implemented only class I must be partially compatible Power Architecture, Class II and III are all processor instructions zCore optional support part. Full ppc405 Instruction Set, see [2] or Appendix A PPC405 instruction set.
### 2.1 Instruction Set
#### 2.1.1 I type instruction
I Power class of instructions to provide basic functionality for zCore compatible with all processors. "Basic Power compatible" here means: to provide "The IBM PowerPC Embedded Environment: Architectural Specifications for IBM PowerPC Embedded Controllers" binary compatible set forth in the user-level programs that support Power instruction set UISA grade all instruction norms embedded environment, VEA portion additionally includes instructions and OEA. Total 191 I type instruction.
In the development process, for ease of implementation and design verification, we will instructions are further divided into Class I subclasses A and B subclasses instructions.
AType of instruction decoding hardware by way of a direct implementation. We have achieved a full 154 A class of instructions
BClass, may be configured to hard-wired, microcode, emulation, software library or the like closed by a compiler compatible manner. include
Multiply instruction 9 - Hardware Implementation
mulhw [.], mulhwu [.], mulli, mullw [o] [.]
Division instruction 8 - implemented in hardware is not employed - achieved by emulation
divw [o] [.], divwu [o] [.]
Memory access instruction with update article 14 - is not achieved, closed by the GNU compiler
lbzu, lbzux; lhau, lhaux; lhzu, lhzux; lwzu, lwzux;
stbu, stbux; sthu, sthux; stwu, stwux;
Complex instruction fetch 6 - unimplemented, closed by the GNU compiler
lmw, lswi, lswx
stmw, stswi, stswx
Part of the hardware logic has been developed, but for the integration and verification.
#### 2.1.2 Instruction Class II
Class II instruction Cache, MMU / TLB related instructions. Wherein four instructions instruction cache, data cache instruction 9 and 6 TLB management instructions, a total of 19. Unrealized, as a NOP operation.
#### 2.1.3 III type instruction
IIIClass of instructions for the MAC, FPU, SIMD, SPE VLE and other associated instructions optional member. 84 wherein the MAC instruction. Unrealized, causing illegal interruption.
Class II and Class III instructions are optional part, does not affect the compatibility of the PowerPC architecture application level.
#### 2.1.4 Analog command
In the current zCore, the instructions for the hardware is not supported, set special emualtion space to simulate the execution of instructions. Spatial Simulation ROM tentatively set 512B, tentatively address (0xffff_fc00 - 0xffff_feff). Address of the instruction ROM simulation can be configured in hardware design (plans to add software can write SPR).
ZCore currently unsupported all instructions can be implemented by an analog instruction, including closed by a compiler directive to support legacy PowerPC processors each legacy binary. At the same time, simulate different ROM configuration can support different versions of the PowerPC binaries.
Instruction simulation for system software and application developers transparent, specific instructions may execute cycle reference manual optimization software.
To improve the performance of an analog instruction, zCore disclosed comprising a plurality of non-special and the like SPR.
### 2.2 Register Group
zCore register group comprise a general purpose register file and the special register set GPRs SPRs. Comprises a total of 32 general purpose registers, condition register CR, and other machine state register MSR special register addressed by SPR, comprising:
CTR and LR registers;
The XER register point exception;
Interrupt control register: DEAR, ESR, EVPR, MCSR, SRR0, SRR1, SRR2, SRR3;
General SPR:
USPRG0
SPRG0, SPRG1, SPRG2, SPRG3
SPRG4, SPRG5, SPRG6, SPRG7
Timer register
TBL, TBU
PIT, TCR, TSR
In addition to the following special description section of the register, zCore support ppc405 defined user mode and supervisor mode all registers and register fields defined functions.
#### 2.2.1 machine state register MSR
ppc405The MSR ppc domain may refer to the user manual [2], which is currently only supports zCore four bit field, as shown below:
Place	Bit domain name	Status Description	Remark
14	CE	Critical Interrupt Enable: / 0 Critical interrupts are disabled / 1 Critical interrupts are enabled	Enable critical interrupts, watchdog timer for the first time out interrupt.
16	EE	External Interrupt Enable: / 0 Asynchronous interruptsare disabled. / 1 Asynchronous interrupts are enabled.	Enable non-critical external interrupts, PIT, and FIT interrupted.
17	PR	Problem State: / 0 Supervisor state. / 1 Problem state.	Processor state setting
19	ME	Machine Check Enable / 0 Machine check interrupts are disabled. / 1 Machine check interrupts are enabled.	/

#### 2.2.2 unrealized SPRs
mmu unrealized SPRs mainly used for the original ppc405 / cache subsystem and debugging subsystem, zCore not support these functions. These registers are all accessible in Privileged mode, comprising:
Processor Version Register: PVR (actually been achieved, but it is not recommended to use the software)
For Cache and MMU configuration register and the like: CCR0, CCR1
Memory Control register: DCCR, DCWR, ICCR, SGR, SLER, SU0R
Protection Domain Register: ZPR
Debug Support Register: DAC1, DAC2, DBCR0, DBCR1, DBSR, DVC1, DVC2, IAC1, IAC2, IAC3, IAC4, ICDBDR

#### 2.2.3 DCRs processing
PPC405 interconnect system uses CoreConnect chip peripheral portion of register map register DCR, / mtdcr mfdcr accessed by the processor. To meet the different on-chip bus, zCore not recommended peripheral configuration register DCR. However, in order to support legacy systems, currently supports zCore mfdcr / mtdcr instructions, and a processor portion tightly bound external controller, an interrupt controller such as a Universal uic and uartlite, mapped to DCRs, zCore to simplify the internal logic, the address is limited to DCR hex "x5x", i.e., the second bit is fixed to 5.
### 2.3 interrupt handling
To facilitate verification and system debugging processor, zCore specification ppc405 addition to achieving the interrupt processing, the other to achieve a special mode, may be arranged in the chip design implementation. The difference between the special mode and ppc405 mode with only a single interrupt vector address relocation and interrupt vector space compression to reduce storage space requirements, to adapt to the most simple system design.
#### 2.3.1 PPC405 interrupt vector table - Normal mode
Interrupt type	Interrupt vector address offset	zCore achieve
Critical input interrupt	0x0100	stand by
Machine check-data / instruction	0x0200	stand by
Data storage interrupt	0x0300	Yet to achieve
Instruction storage interrupt	0x0400	Yet to achieve
External interrupt	0x0500	stand by
Alignment	0x0600	stand by
Program	0x0700	stand by
FPU Unavailable	0x0800	Yet to achieve
System Call	0x0c00	stand by
APU Unavailable	0x0f20	Yet to achieve
PIT	0x1000	stand by
FIT	0x1010	stand by
Watchdog timer	0x1020	stand by
Data TLB miss	0x1100	Yet to achieve
Instruction TLB miss	0x1200	Yet to achieve
Debug	0x2000	Yet to achieve

#### 2.3.2 Special mode interrupt vector table
Interrupt type	Interrupt vector address offset	zCore achieve
Critical input interrupt	0xff00	stand by
Machine check-data / instruction	0xff10	stand by
Data storage interrupt	0xff20	Yet to achieve
Instruction storage interrupt	0xff30	Yet to achieve
External interrupt	0xff40	stand by
Alignment	0xff50	stand by
Program	0xff60	stand by
FPU Unavailable	0xff70	Yet to achieve
System Call	0xff80	stand by
APU Unavailable	0xff90	Yet to achieve
PIT	0xffa0	stand by
FIT	0xffb0	stand by
Watchdog timer	0xffc0	stand by
Data TLB miss	0xffd0	Yet to achieve
Instruction TLB miss	0xffe0	Yet to achieve
Debug	0xfff0	Yet to achieve

At system initialization, interrupt vector processor prefix register is configured to EVPR top address 0xffff. This interrupt handler is positioned at the top of the storage space (iocm). External generic interrupt controller may be the same address offset as hardware configuration parameters, may be provided in subsequent chapters.
In addition, the current zCore implementation, when the non-aligned memory access occurs, will lead to a non-aligned interrupted. Refer to subsequent programming considerations.
### 2.4 Programming Considerations
For zCore system software and application software development, should note the following:
1, when the high-level programming language for the current zCore 200, gcc must add the following parameters:
   "-mcpu = common": 4xx series to avoid generating the dedicated instruction mac
"-mno-multiple" / "- mno-string": Close multi-word instruction and the memory access string
"-mno-update": update to close the base address of the memory access instructions
In addition, zCore temporarily closed hardware divider to reduce resource requirements
2, the system for software developers, close all configuration involves Cache, MMU / TLB or the like, do not use the relevant instructions, the current implementation, zCore the class II as an empty instruction operation (or an exception is thrown).
3, zCore support mfdcr / mtdcr peripheral register access instructions, but the peripheral DCR base address restrictions, particularly with reference to subsequent parts of the system can be described.
4, unaligned access: All unaligned unaligned memory access will trigger an interrupt, includes not only the atomic instruction and cache instruction ppc405 like "lwarx / stwcx.". Here is the definition of non-aligned half-word access refers to the last address of 1, did not address two-word access is not 00 and so on.
5When the register domain zCore not supported by SPR or unimplemented register for access, the behavior is undefined.
### 2.5 Software Development Kit
All development tools for PowerPC / Power Architecture processors can be used in zCore software development, such as Codesourcery, DENX, Ronetix and Macraigo such as GNU and Eclipse-based development suite provided. For consistency, it is recommended to use a series of tools Codesourcery chain.
## 3, zCore processor subsystem

zCore processor subsystem simply referred to as PSS (processor sub-system), as shown in FIG PSS structure, external I / O port includes a transceiver interface, the external interrupt request and the like. PSS contains zCore processor core, a unified instruction and data storage chip (uocm), a timer Timer, supports 32 general-purpose external interrupt source UIC interrupt controller, and a serial communications controller for debugging uartlite. Register access by the timer and mfspr mtspr. uic / uartlite accomplished by mfdcr registers and mtdcr.
### 3.1-chip memory -OCM
On-chip memory properties comprising:
Configurable Size: FPGA configuration depends on the capacity and range of ASIC technology;
uocm access transparent to the programmer - currently does not support configurable base address;
ucomThe entire space to support a "Write / Read / Execute", but use the space defined recommended, to avoid self-modifying code case (self-modify code) use.
Note: There is a cycle of performance loss when uocm be store access to non-word (Byte and Halfword) of.
Uocm entire memory space may be initialized or implemented by rewriting uartlite line mode when a special chip. Examples of the storage space is allocated as follows (when configured as 16KB):
* Address: 0xffff_c000 - 0xffff_ffff.
* 0x0000_0000 - 0xffff_bfff: Non-Available
* 0xffff_c000 - 0xffff_d7ff: RAM, 7KB, "Read / Write", for program run-time data
* 0xffff_d800 - 0xffff_dfff: RAM, 1KB, "Read", for read only data
* 0xffff_e000 - 0xffff_ffff: 8KB, "Execute", for code section, includes:
0xffff_e000 - 0xffff_fbff: user programs
0xffff_fc00 - 0xffff_feff: emulation rom
0xffff_ff00 - 0xffff_fff8: exception vector for special mode
0xffff_fffc: reset vector
The above example is a hardware SIM FEP environment and verify the actual assembler program development environment, specifically refer to supporting sample files. SIM is RTL-level verification environment, FEP for the FPGA emulation system.
### 3.2 Timer -Timer
zCore timer timer specifications comply ppc405, reference ppc405 User Manual [2]

### 3.3 Serial Communication Controller -Uartlite
Uartlite is zCore unique serial communication module, comprising two operating modes. Can be used for the normal mode and pc-machine communication, the downloaded file can be downloaded bin binary mode startup file format by pc-side memory to the processor subsystem iocm. Normal mode and the switching mode set by the download platform hardware switch, refer to the specific use "System Board User's Guide." Currently uartlite 115200 baud rate is fixed, two stop bits, start without software configuration.
Uartlite normal mode programming instructions: four eight-bit registers comprising the following table, internal registers are accessed through mtspr / mfspr instruction
DCR address	Register name	Bit wide	access	Explanation
0x350	TX	32 bit	Write / Read	Send Data Register:
0x351	RX	32 bit	Read-only	Receive data register:
0x352	CTRL	32 bit	Write / Read	Control register:
0x353	STA	32 bit	Read-only	Status Register:

#### 3.3.1 Transmit Data Register TX
Place	0-23	24:31
Bit Description	Retention	Data to be sent

#### 3.3.2 Receive Data Register RX
Place	0-23	24:31
Bit Description	Retention	Receive data

#### 3.3.3 Control Register CTRL
Place	0-26	27	28	29	30	31
Field Description	Retention	Clear Interrupt Request	Receive Interrupt Enable	Transmit Interrupt Enable	Receiving Close	Send start

Note: 1, reset state: 32'h0000_0000
2, Bit [31] / [27] is written, "1" is automatically cleared after

#### 3.3.4 Status Register STA
Place	0-26	27	28	29	30	31
Field Description	Retention	Receiving an interrupt request: Byte 1 indicates a reception completion	Transmit interrupt request: 1 byte sent before completion represents	Interrupt request: 1 indicates presence of transmission and reception completion interrupt request	Reception state: receiving represents 1, 0 means idle	Send Status: 1 indicates busy, idle 0 represents

Programming Note: STA used before reading state STA, you must insert three instructions do not affect the state of STA, STA to wait for the completion of the update.

#### 3.3.5 Uartlite programming examples
Example 1 - programming transmitted character Uartlite
    addis r4, r0, ASCII_O @ h
    ori r4, r4, ASCII_O @ l
    mtdcr DCRN_DSUTX, r4	// data ready
    mfdcr r5, DCRN_DSUSTA
    andi. r5, r5, DSUTX_BUSY
    bne (-8)	// check transmitter status, if busy, waiting
    addis r6, r0, DSUTX_GO @ h
    ori r6, r6, DSUTX_GO @ l
    mtdcr DCRN_DSUCTRL, r6	// send tx command to register dsu_ctrl
Exemplified by the above-described transmission ASCII code "O" (ASCII_O) Workflow: writing data to be transmitted first transmitting register TX, and then sends a status inquiry, if a transmission is complete the busy waiting, and finally transmits a command write control register CTRL. Note that, when uartlite sending, upon receiving the new transmission data, the transmission does not affect the current.
Example 2 - Uartlite programming received character:
    mfdcr r5, DCRN_DSUSTA
    andi. r5, r5, DSURX_DONE
    beq (-8)	// check rx_done bit of STA; if no rx, wait
    addis r7, r0, DSUIRT_CLEAR @ h
    ori r7, r7, DSUIRT_CLEAR @ l
    mtdcr DCRN_DSUCTRL, r7	// clear rx_done bit of STA via clear interrupt
Exemplified by the above-described transmission ASCII code "O" (ASCII_O) Workflow: sending first status query, if the busy wait on completion of a transmission, and then transmits the data to be written to the transmit register TX, sends a command write control register CTRL. A complete sample test file can reference assembly.
Note: 1, uartlite currently working in polling mode, interrupt enable unused. 2, software is responsible for management of the flow control, i.e., if the processor does not process the received data, the next data is received before the completion of the cover; complete after receiving a character, the processor must clear the reception completion flag for the next reception.
## 4, zCore Implementation Guide
Proven processes using Synplify 9.6.2 and ISE 9.1-EDF implementation flow simulation software Modelsim 6.1f.
PippoThe PSS system initially achieved results in the following table:
Design	Frequency	Resource	Device
pippo_core	92.6MHz	RegBits: 2369 (8%); DPRams (RAM32X1D): 96; BMUL: 4; LUTs: 6857 (23%)	Xilinx Virtex II Pro 30 / Xc2vp30fg676-7
pippo_core	40.9MHz	RegBits: 1751 (7%); DPRams (RAM16X1D): 192; BRams: 2 of 28 (7%); LUTs: 7145 (32%)	Xilinx Sparton 3S / xc3s1200eft256-4
top_pss (iocm / docm)	88.7MHz	RegBits: 2203 (7%); DPRams (RAM32X1D): 96; BRams: 72 (52%); BMUL: 4; LUTs: 6591 (22%)	Xilinx Virtex II Pro 30 / Xc2vp30fg676-7
top_pss (uocm)	75MHz	RegBits: 2510 (8%); DPRams (RAM32X1D): 96; BRams: 8 (5%); BMUL: 4; LUTs: 6891 (23%)	Xilinx Virtex II Pro 30 / Xc2vp30fg676-7

## 5, zCore Integration Guide

Referring to FIG SoC shown above, the PSS support by various on-chip interconnect protocols CBU (Core Bridge Unit), other integrated peripherals include UART16550 module, a memory controller, Ethernet MAC controller and SPI / I2C like.
Other specifications to be further supplemented
### 5.1 kernel bridging unit CBU
Currently CBU to complete the integration and verification
### 5.2 Reference SoC
CBU is currently unfinished Wishbone bridges and AMBA bridge.
## 6, FPGA platforms Guide
Xilinx-based platform XUPv2P XUPv2P Development Board [3]. It has been verified zCore actual operating UART and file download capabilities. Details refer Trial / board source code directory.
## Reference Documents
[1] The IBM PowerPC Embedded Environment: Architectural Specifications for IBM PowerPC Embedded Controllers, Version 1.0
[2] PPC405-S Embedded Processor Core User's Manual, Version 1.0
[3] XUP Virtex-II Pro Development System Hardware Reference Manual
## Appendix A: PPC405 Instruction Set
According to functional classification, an instruction set implemented IBM ppc405 summarized as follows:
### a.1 arithmetic and logic instructions
Arithmetic and logic comprises a three-operand instruction formats and two-operand format, and immediate format. [O] represents a command that includes updated XER [SO, OV] "o" in the format, and the "non-o" format;. [[Mean instructions comprise updated CR [CR0] of "record" format, and "non-record" format. 24 which add instruction, add instruction 21, 9 multiplication instruction, division instruction 8 and 4 negative instructions, arithmetic instructions were 64, 28 and logical operation instructions. Note:.. Addic, andi andis instruction code and Rc does not contain a domain. [.]
Arithmetic instructions shown in the following table
Add	Subtract	Multiply	Divide	Negate
add [o] [.] / addc [o] [.] / adde [o] [.] / addi / addic [.] / addis / addme [o] [.] / addze [o] [.]	subf [o] [.] / subfc [o] [.] / subfe [o] [.] / subfic / subfme [o] [.] / subfze [o] [.]	mulhw [.] / mulhwu [.] / mulli / mullw [o] [.]	divw [o] [.] / divwu [o] [.]	neg [o] [.]

The logical operation instructions shown in the following table
And	And with / Complement	Nand	Or	Or with / Complement	Nor	Xor	Eqv	Misc
and [.] / andi. / andis.	andc [.]	nand [.]	or [.] / ori / oris	orc [.]	nor [.]	xor [.] / xori / xoris	eqv [.]	extsb [.] / extsh [.] / cntlzw [.]

### a.2 compare instruction
Instructions for comparing two operands of an arithmetic or logical comparison, and according to the result CR is provided. A total of four instructions.
Arithmetic	Logical
cmp / cmpi	cmpl / cmpli

### a.3 cyclic shift instruction
A total of 14 instructions.
Rotate	Shift
rlwimi [.] / rlwinm [.] / rlwnm [.]	slw [.] / sraw [.] / srawi [.] / srw [.]

### a.4 CR logical instructions
A total of 9 instructions
crand / crandc / creqv / crnand / crnor / cror / crorc / crxor / mcrf

### a.5 branch instruction
An unconditional branch instruction can jump to any address or under certain conditions. First conditional branch instruction to test the condition code of the previous instruction is set, and also change the conditional branch instruction registers CTR test, the return address can be stored in the register LR. Conditional branch target address may be converted from the current address or absolute address, you can also come from LR or CTR. A total of 4 and 8 unconditional jump instruction conditional jump instructions.
Unconditional	Conditional
b / ba / bl / bla	bc / bca / bcl / bcla / bcctr / bcctrl / bclr / bclrl

### a.6 memory access instructions
Memory access instruction for transmitting data between the memory and the GPR, the operand bytes including bytes, halfwords and words halfword words. In addition, memory access instructions also support loading or storing multiple registers, character strings byte-reversed data, and the like. Total 22 18 Load Store instructions and commands.
Loads					Stores
Byte	Halfword / Algebraic	Halfword	Multiple / And / String	Word	Byte	Halfword	Multiple / And / String	Word
lbz / lbzu / lbzux / lbzx	lha / lhau / lhaux / lhax	lhbrx / lhz / lhzu / lhzux / lhzx	lmw / lswi / lswx	lwarx / lwbrx / lwz / lwzu / lwzux / lwzx	stb / stbu / stbux / stbx	sth / sthbrx / sthu / sthux / sthx	stmw / stswi / stswx	stw / stwbrx / stwu / stwux / stwx / stwcx.

### a.7 interrupt control instruction
Interrupt control instruction is used to transfer data between a GPR and the MSR, returning from the interrupt, enable or disable maskable external interrupts. There are 6 instructions.
mfmsr / mtmsr / rfi / rfic / wrtee / wrteei

### a.8 processor management instruction
Processor instructions for managing the exchange of data between a GPR and SPR, provided Traps, system calls and synchronization control. Note DCR relevant directives pending implementation. A total of 14 instructions.
eieio / isync / sync	mcrxr / mfcr / mfdcr / mfspr / mftb	mtcrf / mtdcr / mtspr / sc / tw / twi

### a.9 cache control command (Write support)
Cache control instructions and the following Write TLB management instructions are implemented in pippo. In the implementation of Pippo, temporarily accordance with the NOP; total of 4 and 9 instructions instruction cache data cache instruction.
D-cache	I-Cache
dcba / dcbf / dcbi / dcbst / dcbt / dcbtst / dcbz / dccci / dcread	icbi / icbt / iccci / icread

### a.10 TLB management instructions (not yet supported)
TLB management instructions for accessing the TLB in MMU clauses, TLB search array, and the synchronization failure TLB clause TLB update the other processors. There are 6 instructions.
tlbia / tlbre / tlbsx [.] / tlbsync / tlbwe

### a.11 PPC405 special instructions
Note that the command contains the target part belongs PowerPC405 compatible products, but is not contained in the instructions "IBM PowerPC Embedded Environment" specification. Instructions of 97, wherein 84 is the MAC instruction.
dccci / dcread / iccci / icread	macchw [o] [.] / macchws [o] [.] / macchwsu [o] [.] / macchwu [o] [.] / machhw [o] [.] / machhws [o] [.] / machhwsu [o] [.] / machhwu [o] [.] / maclhw [o] [.] / maclhws [o] [.] / maclhwsu [o] [.] / maclhwu [o] [.]	nmacchw [o] [.] / nmacchws [o] [.] / nmachhw [o] [.] / nmachhws [o] [.] / nmaclhw [o] [.] / nmaclhws [o] [.]	mulchw [.] / mulchwu [.] / mulhhw [.] / mulhhwu [.] / mullhw [.] / mullhwu [.]	mfdcr / mtdcr / rfci / tlbre / tlbsx [.] / tlbwe / wrtee / wrteei